## Slide 1: pH measurements
The probe, from chemistry to voltage to a number
+
+
V

## Slide 2: pH probe
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
Silver/silver chloride electrode
Porous reference junction
4 M KCl solution
Glass bulb (insulator) with anionic sites
+
+
V
Sensing electrode
Reference electrode
Buffered KCl solution

## Slide 3: Glass membrane (Insulator)
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
pH 4 solution (high H+)
Voltage across glass membrane
Solution voltage is 180 mV higher than reference!
We need a way to measure the solution voltage
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
Reference Voltage Call it zero!
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+

## Slide 4: pH Measurements
The porous frit provides electrical contact between the solution and the electrolyte
  Must be in contact with the sample solution
  Probe won’t work well if frit is clogged (fouled)
The voltage measurement requires a very high __________ circuit (high resistance) because a pH probe can’t produce much current
Gentle stirring keeps the solution next to the glass bulb from being depleted of protons
+
+
impedance

## Slide 5: Difficult Measurements?
pH is difficult to measure in poorly buffered solutions
  Distilled water
  Rain
  Between pKs of dilute buffers

## Slide 6: Nernst Equation: Voltage = f(pH)
Reference (known) [H+]
Voltage at
Faraday constant
Gas constant

## Slide 7: Nernst Equation
Chart: pH
| 4 | 10
E at 0 C | 162.2511 | -162.2511
E at 25 C | 177.1011 | -177.1011
E at 35 C | 183.0411 | -183.0411
E at 100 C | 221.6511 | -221.6511

## Slide 8: Slope vs. Temperature
Temperature compensation is important when temperature changes between samples!
Chart: Temperature (C)
| 0 | 99
mV/pH | 54.0837 | 73.6857

## Slide 9: pH Calibration
It would be possible to make a pH measurement without any calibration
  Based on theoretical values
  This is how the software recognizes buffers!
Calibration accounts for non-ideal probe behavior (fouling) as well as electronic measurement errors
It is important that buffers be used covering the range of pH measurements

## Slide 10: The Challenge
E | T | Buffer pH
Current measurement (E, T)
pH
0 to 3 known buffers used as standards
Temperature compensation optional

## Slide 11: Multiple Point Calibrations w/ Temperature Compensation
How would you use this information to calculate pH?
E (mV) | T (C) | Buffer pH
8 | 23 | 7
185 | 24 | 4
-170 | 20 | 10
Current measurement (E, T)
pH
Piecewise linear fit
Calculate E/T